## Slide 1
GRIDSHIELD AI · 01/10
Problem
The grid's sensors can lie — and operators act on it.
▸ Millions of smart meters, inverters and SCADA nodes = millions of entry points
▸ A false-data injection skews what operators see; a hijacked command skews what they do
▸ Energy tools trust all data; security tools don't understand energy
▸ Wrong dispatch, avoidable imports, blackouts — discovered too late

## Slide 2
GRIDSHIELD AI · 02/10
Solution
GridShield AI: predict, protect, optimize — through attacks.
▸ Live digital twin of a solar + battery campus microgrid
▸ AI detects when data lies, explains why, isolates the traitor device
▸ Keeps operating on reconstructed trusted values
▸ Re-optimizes the battery in seconds — resilience, not just alerts

## Slide 3
GRIDSHIELD AI · 03/10
How it works
Twin → AI → response, in one 1-second loop.
▸ Twin: deterministic physics, 5-min steps — solar, battery, grid, 6 buildings, SCADA
▸ AI: forecasters → 5-channel hybrid detector → classifier → explanations
▸ Response: isolate → reconstruct → MPC re-solve → audit log → re-admit
▸ FastAPI + WebSocket backend, React dashboard — runs on a laptop

## Slide 4
GRIDSHIELD AI · 04/10
Digital twin
Two data planes — the core trick.
▸ RAW plane = exactly what SCADA sees (attacked)
▸ TRUSTED plane = what the AI forecasts and controls with
▸ Attacks corrupt the view, never the physics — like real FDI
▸ Twin + attacks + detection in one loop = measurable resilience

## Slide 5
GRIDSHIELD AI · 05/10
AI
Lightweight models, calibrated decisions.
▸ Forecast: solar 10.3 kW / demand 7.1 kW MAE — trained in <1 s
▸ Detect: 5 evidence channels incl. control-plane consistency — the battery must obey the defender's plan
▸ Threshold calibrated at P99.5 of clean traffic → 0.5% false positives by construction
▸ Measured: precision 1.00 · first alert in 1 step · 5/5 attack classes

## Slide 6
GRIDSHIELD AI · 06/10
Cyber defense — live demo
One click, full chain.
▸ FDI_BULK launches; metered load jumps +35% — physics untouched
▸ ATTACK → DETECTION → EXPLANATION → DEFENSE → RECONSTRUCTION → RE-OPTIMIZATION → RECOVERY
▸ Jury-readable explanations: reasons, evidence, threshold, attributions
▸ Same seed ⇒ identical run, every time

## Slide 7
GRIDSHIELD AI · 07/10
Results
Measured, reproducible — never invented.
▸ Detection: precision 1.00 · FPR 0.5% · latency 1 step (all 5 attack classes)
▸ Response: hijack exposure 25 → 5 min; battery deviation −80%
▸ Federated FedAvg: global MAE 7.06 kW = centralized baseline, zero raw data shared
▸ 34 tests green; every number from scripts/run_experiments.py

## Slide 8
GRIDSHIELD AI · 08/10
Impact & scalability
From campus to feeder.
▸ Users: campuses, distribution operators, industrial parks
▸ Value: corrupted-decision minutes avoided; battery assets protected; audit trail
▸ Deploy: same data contract against a real historian; per-feeder detectors; ms per tick
▸ Societal: automation that explains itself in critical infrastructure

## Slide 9
GRIDSHIELD AI · 09/10
Innovation & bonus areas
All five target areas addressed.
▸ Digital twin with two data planes ✓
▸ Explainable AI on every alert ✓
▸ Live cyberattack demonstration (local, safe) ✓
▸ Federated learning FedAvg PoC — weights only ✓
▸ Control-plane detection channel — catches what telemetry-only detectors miss

## Slide 10
GRIDSHIELD AI · 10/10
Conclusion & roadmap
Predict. Protect. Optimize.
▸ Next: real SCADA ingestion (IEC 61850) · probabilistic forecasts · SHAP in production · federated detection · hardware-in-the-loop
▸ The detect → explain → contain → reconstruct → optimize loop is ready today
▸ GridShield AI — trustworthy energy automation under attack
IEEE SmartSecureGrid Challenge 2026 — Proof of Concept (video excluded from repo; recorded separately)